

Associated British Ports South West Wales

Passage Planning,  Navigation & Ordering Of Services Guidelines

| Section | Title | Content | Page |
| --- | --- | --- | --- |
| Section 1 | Introduction | Control of Documentation Amendments Legal Authorisation | 2 |
| Section 2 | Local Port services |  | 4 |
| Section 3 | Navigation and ordering of services Guidelines for South West Wales and the River Usk | Note to Guidelines 1 Compulsory Pilotage 2 Towage Guidelines 3 Allowances and UKC 4 Navigating in Restricted Visibility and / or adverse weather. 5 Ordering of services 6 Pilot Boarding Area 7 Anchorages 8 Passage Planning. 9. Port Talbot 10. Port of Swansea | 6 |

1. Introduction

# Control Of Documentation

The electronic version of this document is controlled and can only be modified by the Marine Management Team. An up to date copy can be found on www.southwalesports.co.uk

Printed versions of this document will be “Non Controlled” and should not be used for reference.

# Amendments

All amendments should be recorded in the relevant pages at the end of this document

# Legal Authorisation

Associated British Ports South Wales is the Statutory Harbour Authority (SHA) and the Competent Harbour Authority (CHA) pursuant to the Pilotage Act 1987, for several ports and Harbours in South Wales including:

- Swansea

- Port Talbot Dock

- Port Talbot tidal Harbour

The following Guidelines have been established and agreed between the Harbour Master South Wales,   South West Wales  CHA Pilots and various Stakeholders including third party towage providers. The information contained in this booklet is intended as a guide to

commercial vessels navigating in the South West Wales  SHA and CHA areas of Jurisdiction and  aims to aid compliance  with local rules and national legislation.

Section 52 of the Harbours, Docks and Piers Clauses Act 1847 is

Incorporated within the British Transport Docks Act 1969 which sets out the powers of a Harbour Master who may give direction for the following purposes.

a) For regulating the time at which and the manner in which any vessel shall enter into, go out of, or lie in or at the Harbour Dock or Pier, and within the prescribed limits, if any, and its position mooring or unmooring, placing and removing whilst therein.

b) For removing unserviceable vessels or other obstructions from the Harbour, Dock, Pier and keeping the same clear.

The local Byelaws   are published separately

And should be used in conjunction with these guidelines.

These guidelines, Byelaws and ABP South Wales  Notice to Mariners can be found on  www.southwalesports.co.uk

2. Local Port Services LPS

1st of July 2010 saw the inception of Cardiff LPS. Based in Cardiff QA House, Cardiff LPS, as well as providing local port services for the port of Cardiff became a coordination service for the Marine activities in the ABP South Wales Ports   with the following aims;

- To discharge ABP’s responsibilities for navigational safety.

- To comply with National and International laws and conventions and with the provisions of the relevant Acts, Orders and subordinate legislation

- To co-ordinate and facilitate the supply of pilots to vessels In SE Wales

- To provide pilots in SE Wales with the necessary information to allow a passage plan to be formulated for the vessel to which they are assigned

- To act as a first point of contact and inform the relevant managers as per the Regional Port Emergency Plan and the Regional Oil Spill Contingency Plan in the event of an incident within the jurisdiction of Associated British Ports  which may or may not require the involvement of other organisations, services or authorities.

- To disseminate appropriate information to relevant managers and departmental heads in relation to situations and incidents that may not necessarily come under the title of ‘emergency’ but are deemed noteworthy.

- To perform a co-ordination role between pilots, rope men, agents, tug services and pilot cutters in the SE Wales area in order to help facilitate the docking and undocking of vessels and associated services.

- To act as the ABP's central point of contact outside normal office hours for all incoming marine inquiries or information, and for the provision of essential advice, co-ordination and information to the shipping and port community.

- To provide a Port Information service which will meet the demands of port users for relevant port related information in a timely and accurate manner.

Cardiff LPS is continuously manned 24 hours a day.

VHF  : Ch 68

Telephones: 08456018870

Fax:               02920835006

Email:	    Southwalesradio@abports.co.uk

Web:		    www.southwalesports.co.uk

In addition to the services of Cardiff LPS , The individual ports of

- Swansea

- Port Talbot

are covered by local port services situated at the relevant ports.  Working details can be found in Admiralty List of Radio Signals (ALRS Vol 6 (1) )

3. Navigation Guidelines for South West Wales

General note to Guidelines.

Port Passage Planning Guidance note (Ref Port Marine Safety Code / IMO resolution A.285 (VIII )

The  Harbour Authority and Harbour Masters’ powers to regulate the time

and manner of ships entry to, departure from and movement within their

waters serve to complement port passage planning. Passage plans are

therefore to be operated and enforced as an adjunct to the powers of

direction.

The object of port passage planning guidance as required by the Port

Marine Safety Code is to ensure that:

- All parties know relevant details of any particular port passage in advance.

- There is a clear, shared understanding of potential hazards, margins of safety, and the ship’s characteristics.

- Intentions and required actions are agreed for the conduct of the port

passage – including the use of tugs and their availability – and any

significant deviation should it become necessary.

The Port Marine Safety Code requires the exchange of certain information

between the Master of the ship and the pilot in conjunction with any VTS /LPS that may be in operation

.

The careful planning of the movements of every ship in the confines of the

port  areas is an essential element of the ABP South Wales Port Marine  Safety Management System.

Pilots make a significant contribution to the safety of navigation in the confined waters and port approaches of which they have up to date knowledge, but it must be stressed that the responsibilities of the vessel's navigational team and the officer of the watch do not transfer to the pilot.

Attention is drawn to the following extract from IMO Resolution A.285 (VIII):

"Despite the duties and obligations of a pilot, his presence on board does not relieve the officer of the watch from his duties and obligation for the safety of the vessel. He should co-operate closely with the pilot and maintain an accurate check on the vessel's position and movements. If he is in any doubt as to the pilot's actions or intentions, he should seek clarification from the pilot and if doubt still exists he should notify the master immediately and take whatever action is necessary before the master arrives."

The Pilot / Master exchange of information needs to be both detailed and

Structured. The LPS supplied information in conjunction with the pilot and

vessel’s passage plan are to be integrated to ensure that both the Pilot and

Master have information needed for an agreed Port Passage Plan. It

should include as a minimum:

- The provision by the Pilot of relevant planned  traffic information, detailed

local navigational knowledge, including his recommended passage plan. Such details will assist the master to update his own passage plan.

- The provision by the Master of precise information, about the ship, its manoeuvring characteristics, its equipment, including details of any defects.

Guideline No 1

Compulsory Pilotage

Pilotage is compulsory  as described in the Pilotage Directions for  the Ports of Swansea and Port Talbot. All boarding and landing  is undertaken to the standards of the Pilotage Code of Practice

The Harbour Master publishes Pilotage Directions on the ABP South Wales website Pilotage Directions

The published Pilotage Directions have provision for strictly risk assessed deviation from the directions.

If the Master of a compulsory piloted vessel chooses not to accept the Pilotage, of the already embarked authorised Pilot, who has been charged with the conduct of the navigation, the Harbour Master may choose to use his powers to direct the Master of the vessel accordingly

Guideline No 2

Towage Guidelines

The Harbour Master publishes towage guidelines on the ABP South Wales  website Towage Guidelines The guidelines clearly describe the formal provision for deviation from the guidelines. If The master of a vessel chooses not to accept the recommendations of the published guidelines  he must inform the Harbour Master of his intentions,  The Harbour Master will risk assess the intended manoeuvre, if necessary, consulting  with one or more authorised Pilots

The Harbour Master may choose to use his powers to direct the Master of the vessel accordingly.

Guideline No 3

Allowances  and Under Keel Clearance (UKC)

The Harbourmaster publishes the following tables of allowances and UKC for the SW Wales ports and approach channels.

Port Talbot Dock

Port Talbot Tidal Harbour

Swansea

The published figures are based upon maintenance levels  that are monitored and maintained by a Surveying  regime and regular maintenance dredging

- It should be noted that in stemming a vessel for one of the South  Wales Ports , consideration should be given to conditions that may have an effect on the actual height of tide in relation to the predicted height of tide. The Harbour Master cannot be held responsible for any cut in the actual tide height.

Guideline No 4

Navigation in restricted Visibility and / or adverse weather conditions

Restricted Visibility

The Harbour Master has set the following procedures for restricted visibility

The ABP South Wales and River Usk Towage guidelines include guidance for towage operations in restricted visibility  Towage Guidelines

For Vessels that are not requiring the services of tugs the following procedure will be used.

Trigger Distances:

- Swansea: The lights on the eastern and western arms of the breakwater viewed from the Pilot Office.

- Port Talbot: The tidal Harbour jetty viewed from Puckey House.

Procedure

When it becomes apparent that the visibility in a specific port is below the trigger distance the docking or sailing of such vessel shall be suspended pending consultation with relevant parties.

It is the responsibility of the Duty lock controller at Swansea or the Berthing man at Port Talbot Puckey House to initiate consultation with the relevant parties as soon as it becomes apparent that adverse weather conditions are forecast or experienced.

Those parties consulted should include, but not be limited to Lock Controllers at the relevant pier head, Pilots, PEC holders, Tug Skippers, Ships Masters, Deputy Harbour Master and/or  Harbour Master.

The aim of this process is to alert all parties to the relevant conditions enabling them to make an informed decision on whether or not to continue with the movement.

During the consultation each of the following elements must be considered:-

- Passage plan

- Other vessel movements within the harbour or harbour approaches.

- A vessel’s ability to maintain a desired track or position.

- Available space on the berth with regard to the proximity of other vessels on adjacent berths.

- The likelihood of the visibility improving in the short term.

- Restrictions / limitations between Lock / Berth or Berth / Lock. E.g. other vessels, container cranes.

- Contingency plans including navigation aid failures.

Adverse Weather Conditions

The Harbour Master has not set definitive parameters for navigating and berthing / un-berthing in adverse weather conditions due to the varying constraints of the individual vessels, berths and manoeuvres involved.

The following will all have a bearing on the ability of a vessel to navigate within the ABP South West Wales  CHA area in adverse weather conditions.

- The configuration and limitations of the vessel and its equipment

- The particular limitations imposed by the  intended manoeuvre

- The particular limitations  imposed by the topography of the intended berth ( with special regard to the prevailing conditions)

- The experience of the Master/ Pilot /tugs crews .

- Limitations imposed by lock operations and or other traffic programmed for the tide

- The availability of tugs and crews

- The boarding and landing of pilots within the operational limitations of the pilot vessels.

On compulsory piloted vessels, the pilot who is charged with the conduct of navigation, after a full assessment of the situation, (including but not limited to the above points) will make a recommendation to the Master regarding the proposed manoeuvre(s)

If The Master of a compulsory piloted vessel chooses not to accept the recommendations of the authorised Pilot He must inform the Harbour Master of his intentions to proceed. Failure to inform the Harbour Authority is an offence under section 15 (3) of the 1987 Pilotage act) .

The published Pilotage directions have provision for strictly risk assessed deviation from the directions.

The Harbour Master may choose to use his powers to direct the Master of the vessel accordingly

On non compulsory piloted vessels, none piloted vessels and on PEC holder vessels, the Harbour Master may also use his powers to direct the Master of that vessel If he feels that the proposed manoeuvres in adverse weather conditions are not safe.

.

# Guideline No 5

# Ordering of Services

Pilots

- All Pilotage  Services for SW Wales are  coordinated  by South Wales Pilots.

- All Pilotage  Services must be ordered through an appointed agent who is  registered on the Agents Online portal www.abpnotify.co.uk

- The notification  email that is generated by Agents Online (AOL) and sent automatically to the relevant Local Port services  does not constitute an  order for a pilot .

- To Make an order for a  Pilot  , an appointed Agent must ring South West Wales Pilots directly,

- Pilot Cutter Services ( third Party Work)  are arranged via the Pilotage manager.

Procedure

- In Order for the pilot rota to work efficiently,  South West Wales Pilots  need to collate the orders to make best use of the pilots and consider availability of locks, tugs and associated services. It follows that South West Wales Pilots   will try to accommodate timings for boarding’s / sailings where possible but a particular time cannot be guaranteed nor is the tidal program formulated on a first come first served basis.

Notes on Cancellations and late ordering

- There may be situations that pilots will need to be ordered late or cancelled.  This is  unavoidable

- Unnecessary late ordering, or  ordering a pilot  when it is clear that he will be cancelled detracts from the efficiency of the rota system and should be avoided wherever possible, even where such an order or cancellation is not chargeable under the criteria

- contrary to ensuring a pilot will be available, a speculative  pilot order, made with the intention of cancelling it before any  charging  criteria cuts in has a negative effect on pilot availability

Towage ,  Ropemen and Boatmen Services

All   the above services are provided by  third party suppliers.  Swansea and Port Talbot Local Port Services  are not responsible for the ordering of the above services, it is for each vessel / agent to make the necessary arrangements.

# Guideline no 6

# The Pilot Boarding Area

There are 2 pilot Boarding positions Marked on BA Charts

Deep Draft vessels for Port Talbot board in the outer Pilot Boarding Area 6.5m SSW of Mumbles head

Smaller Vessels Board at the Inner Pilot Boarding Area 1m SE of Mumbles Head

Mariners are advised to use extreme caution while navigating  in these areas as  both inbound and outbound vessels are converging and / or manoeuvring to  embark /disembark their pilots.

There are strong tidal streams in this area, the effect of which are accentuated by the slower speeds of vessels  getting underway and manoeuvring for the pilot boarding area

# Guideline no 7

# Anchorages

Note:- South Wales  Local Port Services of Swansea and Port Talbot  or South west wales Pilots do not designate anchorage positions for vessels using the South  West Wales ports. This is an onboard decision to be made by the Master.

There follows below , some anchorage information that Mainers may find useful. However the decision as to the suitability of a particular  anchorage for a particular vessel is a decision for the  Master of the Vessel.  Details are available in the Admiralty publication NP37 West Coast of England and Wales Pilot.

The principal anchorage for deep drafted vessels is situated approximately 7 Miles SSW of Mumbles head and is marked on Chart s

BA 1195

BA 1179

The Anchorage is Marked by a Magenta box and encloses the Pilotage boarding are for Port Talbot

Larger vessels bound for Swansea usually anchor in marked anchorage in the vicinity of the Swansea Pilot Boarding area , SE of Mumbles head

Smaller vessels bound for Swansea or Port Talbot Dock have found good anchorages off Mumbles Roads and the Green Grounds.

There are strong tidal streams in the anchorage  areas, the effect of which are accentuated by the slower speeds of vessels  getting underway and manoeuvring for the pilot boarding area

# Guideline No 8

# Passage planning between Pilot Boarding Areas and Swansea / Port Talbot

The start of this section gives general  Port Passage Planning Guidance based on the   Port Marine Safety Code / IMO resolution A.285 (VIII )

As per this guidance it is for the Mariner to ensure that  passage planning is completed berth to berth and to ensure that the plan is suitable for the specific passage of the specific vessel at the specific time.

SW Wales CHA Pilots will complete the following Pilots passage plan &  Master / Pilot Exchange record form for each act of Pilotage that they perform.

The following British admiralty charts are available for the intended passage

- BA 1179 The Bristol Channel

- BA 1161 Swansea Bay

- BA 1165 The Bristol Channel, Worms Head to Watchet

The following publications should be consulted :-

- Admiralty tidal streams Atlas  NP256 – Irish sea and Bristol Channel

- Admiralty sailing Directions NP 37- West Coast of England & Wales Pilot

- Admiralty List of Light and Fog Signals NP74 – Vol A

Admiralty List Of Radio signals NP287 (Vol6 part 1)

# Guideline No 9 Port Talbot

# Port Talbot

Port Talbot Tidal Harbour operates on a 24 hour basis dependent on draft

ABP South Wales publish acceptance tables on the south Wales ports website. Port Talbot Tidal Harbour  Berth clear times are set to allow sufficient time for the outbound vessel to clear the approach channel before the

inbound vessel is committed. These safety parameters will not be compromised .

Vessels should not proceed inwards or outwards from the tidal harbour without the permission of Port Talbot Harbourmasters. Full procedures are  available in ALRS  volume 6 (1)

Admiralty Publication NP 37 gives local Pilotage and anchorage  information

Commercial vessels are berthed and un-berthed within the tidal window according to a tidal plan that is collated by  Swansea / Port Talbot Pilots with input from Swansea  Lock Controllers and  Port Talbot Harbourmasters . The tidal plan is not based upon a first come first served basis but will consider many parameters  including but not limited to :

- Draft of Vessel

- Weather conditions

- Range of tide ( spring / Neap)

- Availability of tugs

- Considerations of owners/agents

- Ordering  and availability of pilots and to make best use of  those available pilots

There are strong cross currents in the approach Channel and harbour entrance

The Harbour entrance and approach channel  are very exposed to Winds from West through to South

# Port Talbot Docks

Port Talbot Dock operates on a tidal basis (nominally 4 hrs before to 4hrs after HW)  Though in practice , vessels will be stemmed to transit the lock and channel around HW

ABP South Wales publish acceptance tables on the south Wales ports website. Port Talbot Dock

Vessels should not proceed inwards of the Stalheim wreck  buoy or outwards from the  Lock without the permission of Port Talbot Harbourmasters . Full procedures are available in ALRS volume 6 (1)

Admiralty Publication NP 37 gives local Pilotage and anchorage information

Commercial vessels are locked in and out within the tidal window according to a tidal plan that is collated by  Swansea / Port Talbot Pilots with input from Swansea  Lock Controllers and  Port Talbot Harbourmasters. The tidal plan is not based upon a first come first served basis but will consider many parameters including but not limited to:

- Draft of Vessel

- Weather conditions

- Range of tide ( spring / Neap)

- Availability of tugs

- Considerations of owners/agents

- Ordering  and availability of pilots and to make best use of  those available pilots

An inbound vessel that is not capable of turning and exiting   the approach Channel should not pass the point of no return (a position to the West  of the Stalheim wreck buoy that it can safely turn around given the constraints of the vessel, weather and tide) until it has been advised that the lock is ready in all respects .

The approach to Port Talbot Lock is particularly open to winds from the West Through to South the following controlling factors will dictate entry and exit

- Sufficient height of tide in relation to draft  and swell conditions

- The ability to maintain steerage way at a suitable speed for safe entry

# Guideline No 10 Swansea

# Port of Swansea

The Port of Swansea  operates on a tidal basis (nominally 4 hrs before to 4hrs after HW)  Though in practice , most  vessels will be stemmed to transit the lock and channel around HW . There is a ferry RO-RO berth in the outer harbour that is serviceable on a 24hr basis provided the  draft of the vessel provides sufficient UKC for both Channel passage and Low water Lay over on the berth

ABP South Wales publish acceptance tables on the south Wales ports website. Swansea

Vessels bound for the lock  should not proceed inwards of the SWIGG ( South West Inner Green Grounds) buoy or outwards from the  Lock without the permission of Swansea Port Control . ( does not apply to vessels with an agreed schedule that includes off tide arrivals and / or sailings) Full procedures are available in ALRS volume 6 (1)

Admiralty Publication NP 37 gives local Pilotage and anchorage information

Commercial vessels are locked in and out within the tidal window according to a tidal plan that is collated by  Swansea / Port Talbot Pilots with input from Swansea  Lock Controllers and  Port Talbot Harbourmasters. The tidal plan is not based upon a first come first served basis but will consider many parameters including but not limited to:

- Draft of Vessel

- Weather conditions

- Range of tide ( spring / Neap)

- Availability of tugs

- Considerations of owners/agents

- Ordering  and availability of pilots and to make best use of  those available pilots

An inbound vessel that is not capable of turning in the outer harbour and exiting   the approach Channel should not pass the point of no return (a position to the South of the SWIGG buoy that it can safely turn around given the constraints of the vessel, weather and tide) until it has been advised that the lock is ready in all respects .

The approach to Swansea Port  is particularly open to winds from the South West Through to South East